## Slide 1: 2021 Adequacy Assessment Policy Issues and Future Assessments Resource Adequacy Advisory Committee
Steering Committee Webinar
March 25, 2016

## Slide 2: Policy Issues
What loads should be used?
How should EE be counted?
Should we count “expected” DR?
How to count resources without firm fuel?
How should import limits be set?
Should we address market friction?
Future Assessments – GENESYS redevelopment

## Slide 3: Hourly Loads Short-Term Load Model
Summary | 8,760 hourly loads (rows) for 80 temp years (columns) No leap year data Does include projected EE savings New codes and standards are not accounted for East/West load split factors 0.39/0.61
Lead | Massoud Jourabchi (Council)
Source | Short-term load forecasting model
File Name | HourlyLoadsSTM.bin
Format | Binary file
Status | Yet to be converted into binary format
Location | Adequacy/2016 for 2021/Data/Loads

## Slide 4: Hourly Loads Long-Term Load Model
Summary | 8,760 hourly loads (rows) for 80 temp years (columns) No leap year data Does not include any projected EE savings New codes and standards are accounted for East/West load split factors 0.39/0.61 Loads stretched to user input quarterly peak/mean values
Lead | Massoud Jourabchi (Council)
Source | Long-term load forecasting model Load Stretching program
File Name | HourlyLoadsFE.bin
Format | Binary file
Status | Yet to be converted into binary format
Location | Adequacy/2016 for 2021/Data/Loads

## Slide 5: Recommendation for Loads
Start with the LTM low, medium and high
Update with new data, if available
“Calibrate” quarterly mean and peak loads (yet to be specified how)
Stretch STM hourly loads to match calibrated quarterly mean and peak loads from LTM
Shrink loads by expected EE and DR savings out of the current power plan

## Slide 6: Recommendation for Energy Efficiency
Expected EE savings are derived from the RPM
Quarterly mean and peak savings are the RPM average values from over all games
These values are incorporated into the hourly load forecast

## Slide 7: Recommendation for DR
Include expected new DR (like expected EE)
Minimum DR acquisition (600 MW) from RPM
Quarterly mean and peak DR availabilities are the minimum (percentile?) RPM values
These availabilities are added to the existing standby resource availabilities that are used to assess the final adequacy assessment (via a post processing program)

## Slide 8: Recommendation for Fuel Limitations
Example: Gray’s Harbor
  IPP without firm fuel contract
  Already limited to about 33% capacity for summer
Recommendation:
  Ref Case: No limitations for 2021 assessment
  Scenario: Remove Gray’s Harbor
  Future assessments; add logic to reduce Gray’s Harbor’s availability as a function of temperature

## Slide 9: Imports
Two types
  Purchase Ahead: during light-load hours when forecasting shortage
  Spot Market: during hours with shortages
Maximum Import
  More supply than intertie capability, thus
  Set import limits based on intertie capability
  Update 95th percentile S-to-N monthly capability annually
Recommendations
  2,500 MW spot market, all hours winter only
  3,000 MW purchase ahead, all LLHs year round

## Slide 10: Market Friction
Idea that during shortages utilities will hold on to more reserves and reduce the available market supply
Since this concept focuses on within-region exchanges, the only way to model this is to increase the number of nodes in the region, not recommended at this time
Recommendation:
  No adjustments for 2021 assessment
  Future assessments, add logic to reduce IPP availability as a function of temperature?

## Slide 11: Future Assessments GENESYS Redevelopment

## Slide 12: Some Future Enhancements
Plant-specific hourly hydro simulation
DR and storage simulation logic
Import uncertainty as a random variable
Fuel uncertainty (Gray’s Harbor availability a function of temperature)
Market friction (2 options)
  IPP availability as a function of temperature
  Break up NW into more nodes?
Economic load uncertainty as a random variable