## Slide 1: GENESYS Current Functionality
GENESYS Redevelopment Stakeholder Meeting
March 17, 2016

## Slide 2: Why Review Current State?
GENESYS – GENeration Evaluation SYStem
Multiple Users – Currently used by the Council, BPA and other regional stakeholders.
Multiple Uses – Used for annual regional adequacy assessments, regulated hydro flow studies, and analysis of lost revenue due to hydro dispatch change.
Notes: Needs to be discussed out explicitly
1) Prevent leaving important functionality behind.
2) Challenging because different users use the model to support a variety of analytics.
Multiple Users – Currently used by the Council, BPA and other regional stakeholders.
Multiple Uses – Used for annual regional adequacy assessments, regulated hydro flow studies, and analysis of lost revenue due to hydro dispatch change.

## Slide 3: What Does the Model Do Now?
Performs hourly simulation of FCRPS hydro and regional thermal resource generation under varying stochastic inputs:
Temperature variation (load)
Wind generation
Water supply
Thermal forced outages.
Incorporates constraints on FCRPS, transmission, and limited external market supply.
Notes: The dispatch of resources is actually accomplished using resource stacking instead of evaluating each resource against a set electricity market price.

## Slide 4: Periodic Hydro Block Evaluation
Notes: HydSim is run four times to create these 5 Hydro blocks based on the rule curves for each modified streamflow condition.
This chart illustrates the use of rule curves to guide the operation of the hydroelectric projects more graphically.
For any given month, the rule curve elevations can be “painted” onto the dam itself. The water behind the dam can then be separated into volumes or “blocks.”
Water above the flood control curve is very cheap because it would have to be evacuated even in the absence of a market for that electricity.
Water below the critical rule curve is very, very expensive and can only be used in emergency situations and only for a short time. The water must then be replaced as soon as possible.
Water in the intermediate blocks becomes more valuable the deeper the project is drafted.
Each month, every dam is drafted to its refill curve and the corresponding generation is calculated.
If more generation from the hydroelectric system is desired, every dam is further drafted to its actual energy regulation curve. If this is still insufficient then all projects are again further drafted to their respective critical rule curves.
To “zero in” on the desired amount of hydroelectric energy, the system is drafted “proportionally” between rule curves.

## Slide 5: Functional Simulation Flow
For each window
For each Period
Available hourly hydro energy from shaping the daily energy into the hourly shapes constrained by the peak vs. energy curves
Hourly hydro is dispatched dynamically with thermal resources
Get hydro block sizes
Build resource stack
Build load stack
Hydro and thermal energy for month
For each hour
Window hydro-thermal energy = period load times (historical average window load/period load)
For each day
Daily hydro-thermal energy = window load times (daily load/window load)
If deficit, allow purchase-ahead for the month
If deficit, allow purchase-ahead for the window
If deficit, allow purchase-ahead for the day
If deficit, can use remaining market and then borrowed hydro.
Notes: Period: For a particular hydro, load and wind sample the simulation starts. Forced outages are simulated in the hourly step.
Load here is actually load net wind net long term obligations.

## Slide 6: How Does It Simulate Hourly?
October
Week 1
Sunday
...
Week 2
Period
Window
Daily
Hourly
1
...
24
Week 4
Week 3
2
23
Saturday
Emergency Resources
Notes: This is an example for October.

## Slide 7: Resource Stacking Order
Resource | Description
Firm Hydro and Thermal | From lowest to highest operating cost
Non-firm and Markets | In-region and out-of-region markets, surplus hydro, borrowed hydro
Standby Resources Type 1 | Distributed Standby Generation, Pumped Hydro, ...
Standby Resources Type 2 | Demand Response
Emergency Action 1 | More expensive non-declared resources or contract provisions
Emergency Action 2 | Governor’s call for conservation
Emergency Action 3 | Rolling black outs or brown outs
Modeled in GENESYS
Modeled in Post Processor
Not Modeled

## Slide 8: Model Outputs for Adequacy Studies
Adequacy metrics (LOLP, CVaR, EUE, LOLH, etc.)
  Calculates frequency, duration and magnitude of events.
Regional reliance on market and standby resources
Monthly assessment of potential shortfalls
  Provides insight into conditions under which events occur

## Slide 9: Model Outputs for Regulated Hydro and Lost Revenue Studies
Regulated Hydro Studies
  Generation
  Bypass Spill
  Reservoir Elevations
  Regulated Flows
Lost Revenue
  Compare generation under two different input assumptions.

## Slide 10: Discuss Other Uses of GENESYS?
BPA
Other Stakeholders